## Slide 1
Problem decomposition and approximation for shared mobility applications with endogenous congestion: integrated vehicle assignment and routing in capacitated transportation networks:
Jiangtao Liu (jliu215@asu.edu)
Xuesong Zhou (xzhou74@asu.edu)
School of Sustainable Engineering and the Built Environment
Pitu Mirchandani (pitu@asu.edu)
School of Computing, Informatics, and Decision Systems Engineering
Arizona State University

## Slide 2
  2. Key Elements
  3. Space-Time-State Network Flow Models
  5. Decomposition: Column-pool based approximation
Outline
  6. Discussion and Preliminary Experiments
  1. Introduction
  7. Summary
  4. Decomposition: Dantzig-Wolfe decomposition

## Slide 3
Vehicle Supply
Travel Demand
Vehicle Routing Problem
Dynamic Traffic Assignment
Infrastructure Design
How to optimize demand, supply and infrastructure?
1. Introduction

## Slide 4
Vehicle Routing Problem:
Input:
Network: Virtual point-to-point network
Passenger trip request: has specific pick-up and drop-off location with time windows
Vehicle carrying capacity: considered
Goal:
System Optimal
Output:
Vehicle-to-passenger assignment: will be found
Variable: discrete vehicle routing and scheduling
1. Introduction

## Slide 5
Traffic Assignment Problem:
Input:
Network: Physical traffic network
Road capacity: capture road congestions
Origin and Destination: vehicle has the same origin and destination with the assigned passengers
Goal:
System Optimal or User Equilibrium
Output:
continuous vehicle flow on links/paths
1. Introduction

## Slide 6
1. Introduction
Travel Demand | Vehicle Supply | Infrastructure
Trip request: origin and destination with self-owned vehicles or submit pickup and drop-off locations with time windows for mobility providers Trip privacy: alone or rideshare Trip mode: single mode or multiple modes | Driving mode: self-driving or human-driven Routing behavior: selfish or coordinated Ownership: household or mobility providers | Link/Lane capacity change Sensor and communication (V2V, V2I) Smart Transportation network (road, parking, depots, bus line, rail transit line, etc.)
Uncertain elements from the current to the future

## Slide 7
Keywords:
Physical traffic network to consider traffic congestion
Trip requests with Pickup and delivery with time windows
Autonomous vehicles with carrying capacity for ride sharing
Central control (System optimal)
1. Introduction
Special scenario: integration of travel demand, vehicle supply and infrastructure capacity

## Slide 8
Key questions:
How many autonomous vehicles do we need?
How many passengers can we serve?
How to capture the new traffic congestion?
What is the best vehicle routing and vehicle-to-passenger assignment solution?
1. Introduction

## Slide 9
1. Introduction
# of nodes | 1320
# of links | 5431
optimization time horizon (min) | 60
arc capacity each min (vehicle) | 35
# of passenger groups with same OD and departure time | 2226
Total trip requests | 4452
# of vehicle depots | 243
Chicago Sketch Network

## Slide 10
Link Capacity
Without link capacity:
Total cost is 6
With link capacity:
Total cost is 15
2. Key Elements

## Slide 11
System Optimal Coordination
Without coordination (selfish routing):
Total cost is 15
With coordination:
Total cost is 9
2. Key Elements

## Slide 12
Time windows
The red vehicle can wait until time 3 to pick up passenger 2, so the blue vehicle can pick up passenger 1 at exact time 3.
The optimal result doesn’t only optimize the vehicle routing, but also the departure time of picked up passengers.
Total cost is 9
2. Key Elements

## Slide 13
Ridesharing (vehicle carrying capacity)
When the red vehicle’s carrying capacity is increased to 2, the total cost is reduced to 4 from 9;
Only the red vehicle is required to serve the trip requests.
Total cost is 4
2. Key Elements

## Slide 14
3. Space-time-state network and model formulation
Add virtual pick-up and drop-off nodes and links for each passenger
Passenger trip requests: pickup and drop-off locations and time windows

## Slide 15
Time-extended Space-time network construction for physical path
Arc (i,j,t,s) with capacity
Vertex (i,t), (j,s)
Passenger pickup time windows and locations are embedded in this network
3. Space-time-state network and model formulation
Space-time network

## Slide 16
Vehicle Carrying States for passenger pickup and drop-off:
which passengers are being carried by this vehicle:
To record the passenger service status:
  0: the passenger is not served;
    1: under served (picked up but not delivered);
    2: finished (delivered)
Example: In the case: if vehicle capacity is 1 and 2 passengers trip requests,
All possible states: [ ], [1[1]], [1[2]], [2[1]] or [2[2]]
3. Space-time-state network and model formulation

## Slide 17
Vehicle State Transition with specific pickup and drop-off locations within time windows
Vehicle carrying state transition graph
3. Space-time-state network and model formulation

## Slide 18
One possible vehicle trajectory in a space-time-state network
Vertex:
Arc:
space
state
3. Space-time-state network and model formulation
time

## Slide 19
Arc-based agent-based formulation:
3. Space-time-state network and model formulation
Remark: state definition w differs for passenger pickup only and passenger pickup and drop-off

## Slide 20
Path-based flow-based formulation:
3. Space-time-state network and model formulation
Assumptions:
(1) Vehicles and Passengers can be grouped by its origin, destination and required service time period
(2) All possible paths of vehicle groups can be enumerated in advance.
(3) The space-time-state path of each vehicle group has the mapping information about vehicle-to-passenger and vehicle-to-arc relation.
Pick up passenger 2
Drop off passenger 2
Space-time arc

## Slide 21
Path-based flow-based formulation:
3. Space-time-state network and model formulation

## Slide 22
3. Space-time-state network and model formulation
Simplified format of our models
1. Primal problem
Flow-balance constraint
Coupling constraint (trip request, link capacity)
2. Lagrangian Relaxation
3. Cutting plan method
4. Column generation/DW
Restricted master problem
Subproblems
5. Augmented Lagrangian

## Slide 23
4. Dantzig-Wolfe Decomposition
Objective function
Flow-balance constraint for each vehicle
Coupling constraints (passenger pickup, road capacity)

## Slide 24
Restricted Master Problem
Sub-Problems
4. Dantzig-Wolfe Decomposition

## Slide 25
https://ocw.mit.edu/courses/sloan-school-of-management/15-082j-network-optimization-fall-2010/lecture-notes/
4. Dantzig-Wolfe Decomposition

## Slide 26
4. Dantzig-Wolfe Decomposition

## Slide 27
Restricted master problem
4. Dantzig-Wolfe Decomposition

## Slide 28
Subproblems (TDSDSP)
Dual price of of passenger pickup constraints
Dual price of congestion constraints
Dual price of path weight constraints
4. Dantzig-Wolfe Decomposition

## Slide 29
(1) Pickup requests on passenger group :
(2) Road capacity constraints:
(3) Positive continuous variable (path vehicle flow):
Each column is a path with information and connection of passenger trip requests, and vehicle passed space-time arcs
5. Column-pool based Approximation
Compared with arc-based formulation, column-based model greatly reduces the number of variables.

## Slide 30
5. Column-pool based Approximation
Column\ trip requests | p1 | p2 | p3 | p4
y1 | 1 | 1 | 0 | 0
y2 | 0 | 1 | 0 | 1
y3 | 0 | 0 | 1 | 1
Column\space-time arc | arc 1(i,j,t,s) | arc 2(i,j,t,s) | arc 3(i,j,t,s) | arc 4(i,j,t,s)
y1 | 1 | 0 | 0 | 1
y2 | 0 | 1 | 1 | 0
y3 | 1 | 0 | 0 | 1
Incidence matrix of column with arc
Incidence matrix of column with passenger trip requests

## Slide 31
5. Column-pool based Approximation

## Slide 32
Alternating Direction Method of Multipliers (ADMM)
5. Column-pool based Approximation
Objective function:
Solutions:
Multiplier update:

## Slide 33
Sequentially solving each subproblem
5. Column-pool based Approximation

## Slide 34
Arc-based Agent-based formulation
At each iteration:
Solve each sub-problem sequentially for each vehicle
Each sub-problem is a time-dependent state-dependent shortest path problem for each vehicle
Update Lagrangian multipliers for passenger pickup constraints and arc capacity constraints
5. Column-pool based Approximation
Objective function:

## Slide 35
5. Column-pool based Approximation
ADMM for agent-based model

## Slide 36
At each iteration for each vehicle:
5. Column-pool based Approximation

## Slide 37
Flow-based path-based ADMM:
Quadratic objective functions:
5. Column-pool based Approximation
Its Hessian Matrix can be derived as,
Since it is difficult to directly obtain its inverse matrix , especially in large-scale networks, we apply ADMM to decompose the primal problem to sequentially solve the subproblem for each column.

## Slide 38
Solve each variable sequentially by ADMM
Flow-based path-based ADMM:
5. Column-pool based Approximation

## Slide 39
5. Column-pool based Approximation
Projected Gradient Method (Rosen, 1960) to solve each subproblem
Projected Gradient Method has been used in solving the path-based nonlinear programming models in equilibrium traffic assignment ( Larsson and Patriksson, 1992; Jayakrishnan et al, 1994; Florian et al., 2009), and it is more efficient, compared with arc-based nonlinear programming models, but needs more memory use.

## Slide 40
Beam-search algorithm for finding the time-dependent state-dependent shortest paths:
5. Column-pool based Approximation

## Slide 41
Discussion: path marginal cost calculation
System-impact of adjusting one vehicle routing:
System marginal vehicle travel cost
System marginal passenger service benefit/cost
[Time window]
[Time window]
In this queuing system:
Waiting time for individual: 4 min
After adding one more person in the queue:
Societal travel time: additional 4 min for each person behind: +16 min, and the waiting time of added person is 4 min, so the system marginal waiting time is 20 min.
Societal service benefit: some persons may not be served in their preferred time window and it decreases the service benefit.
6. Discussion and Preliminary Experiments

## Slide 42
Marginal cost calculation in system optimal dynamic traffic assignment (SODTA)
Ghali and Smith (1995)
Ghali, M.O. and Smith, M.J., 1995. A model for the dynamic system optimum traffic assignment problem. Transportation Research Part B: Methodological, 29(3), pp.155-170.
6. Discussion and Preliminary Experiments

## Slide 43
Step 1: Build virtual pickup and drop-off links in physical traffic networks, and its service pricing is converted to generalized link travel cost
Step 2: find one initial solution as the input
Step 3: Perform network loading within a space-time-state network
  3.1 use cumulative arrival and departure counts to derive the link marginal travel cost.
  3.2 update the marginal service link benefit of passengers (not served or served by multiple vehicles)
Step 4: find the new least-marginal-cost route for each vehicles, and go to step 3; otherwise, stop.
Path marginal cost is probably related to the Lagrangian multipliers in ADMM and the dual prices in Dantzig-Wolfe decomposition.
6. Discussion and Preliminary Experiments

## Slide 44
Capture queue spillback:
6. Discussion and Preliminary Experiments

## Slide 45
There are 2 vehicles, and each vehicle picks up one passenger from origin node 1 to destination node 4.
Our goal is to minimize the total vehicle travel cost by using Dantzig-Wolfe decomposition approach.
6. Discussion and Preliminary Experiments

## Slide 46
Iteration 1 | Sub problem | New column: path 4
 | Master problem | , , , , , , ,
Iteration 2 | Sub problem | New column: path 1
 | Master problem | , , , , , , ,
Iteration 3 | Sub problem | New column: path 3
 | Master problem | , , , ,, ,, ,
Iteration 4 | Sub problem | New column: path 2
 | Master problem | , , , ,, ,, ,
Iteration 1 | Sub problem | New column: path 4
 | Master problem | 
Iteration 2 | Sub problem | New column: path 1
 | Master problem | 
Iteration 3 | Sub problem | New column: path 3
 | Master problem | 
Iteration 4 | Sub problem | New column: path 2
 | Master problem | 
The reduced cost is and reach the optimal solution.
6. Discussion and Preliminary Experiments
Variable is the weight of path of total demand; is the dual price of capacity constraint of link ; is the dual price of path flow weight constraint.

## Slide 47
Sioux Falls Network
# of nodes | 24
# of links | 84
# of trip requests (pickup and drop-off with time windows) | 30
# of available autonomous vehicles | 30
# of depots | 5
optimization time horizon (time unit) | 110
Vehicle capacity (person) | 1
Source code: https://github.com/TonyLiu2015/VRPLite-DW
Requests with pickup and drop-off and time windows under capacitated networks
6. Discussion and Preliminary Experiments

## Slide 48
Vehicle_No | Passenger_No | Vehicle_No | Passenger_No | Vehicle_No | Passenger_No
1 | [15] | 11 | [20] | 21 | [23]
2 | [8] | 12 | [26] | 22 | [25]
3 | [1] | 13 | [16] | 23 | [22]
4 | [7] | 14 | [18] | 24 | [19]
5 | [9] | 15 | [2] | 25 | [4]
6 | [11] | 16 | [10] | 26 | [5]
7 | [29] | 17 | [3] | 27 | [24]
8 | [28] | 18 | [12] | 28 | [14]
9 | [17] | 19 | [27] | 29 | [13]
10 | [21] | 20 | [30] | 30 | [6]
Initial feasible solution
6. Discussion and Preliminary Experiments

## Slide 49
Dantzig-Wolfe decomposition algorithm solution:
 | Number of required vehicles | Total travel cost
Initial solution | 30 | 1096
vehicle carrying capacity is 1 | 27 | 967.5
vehicle carrying capacity is 2 | 25 | 869.5
Each passenger has specific pickup and drop-off location and time windows
The vehicle benefit of serving one passenger is 20
The vehicle waiting cost is the half of the waiting time
Take vehicle 9 as an example:
In initial solution: picks up passenger 17 -> drops off passenger 17;
Vehicle carrying capacity is 1: picks up passenger 17 -> drops off passenger 17-> picks up passenger 29 -> drops off passenger 29
Vehicle carrying capacity is 2: picks up passenger 17 -> drops off passenger 17-> picks up passenger 30-> picks up passenger 29-> drops off passenger 29-> drops off passenger 30
6. Discussion and Preliminary Experiments

## Slide 50
# of nodes | 1320
# of links | 5431
optimization time horizon (time unit) | 60
Chicago network
Requests with pickup only and time windows under capacitated networks
6. Discussion and Preliminary Experiments

## Slide 51
Step A: Prior generation of column pool
6. Discussion and Preliminary Experiments
Scenario 1: Sample data set
10 pairs of vehicle groups and passenger groups.
Each pair has 243 vehicles and 387 passengers trip requests
The space-time arc capacity in each minute is 5.
Vehicle carrying capacity is 1
2430 binary variables and 332,160 constraints
Scenario 2: Sample data set
20 pair of vehicle groups and passengers groups.
Each pair has 243 vehicles and 387 passengers trip requests
The space-time arc capacity in each minute is 5.
Vehicle carrying capacity is 1
4860 binary variables and 338,460 constraints

## Slide 52
Solution from Agent-based ADMM
6. Discussion and Preliminary Experiments
Scenario 1:
1789 vehicles find their paths/columns to serve 1084 passengers
23,357 space-time arcs are generated based on vehicles’ space-time paths
Computation time: about 70 seconds each iteration
Scenario 2:
3686 vehicles find their paths/columns to serve 2226 passengers
36,454 space-time arcs are generated based on vehicles’ space-time paths
Computation time: about 140 seconds each iteration
Remark: each passenger has a specific pickup location, time window and destination, and vehicle can only pick up passengers within a same pair of groups.

## Slide 53
Step B: Flow-based ADMM implemented by C++
6. Discussion and Preliminary Experiments
Experiment 1:
1084 passenger groups and each passenger group has 4 passenger trip requests
The space-time arc capacity in each minute is 35
1789 positive continuous variables and 24,441 constraints
Computation time: 700 CPU seconds for running 250 iterations
Experiment 2:
2226 passenger groups and each passenger group has 2 passenger trip requests
The space-time arc capacity in each minute is 35
3686 positive continuous variables and 38,680 constraints
Computation time: 2735 CPU seconds to finish 250 iterations

## Slide 54
Experiment 1
6. Discussion and Preliminary Experiments
Case 1: and ; Case 2: and ; Case 3: and .
Solution of each iteration of ADMM in three cases and CPLEX

## Slide 55
Experiment 1
6. Discussion and Preliminary Experiments
Comparison of objective values of upper bound and CPLEX

## Slide 56
Experiment 2
6. Discussion and Preliminary Experiments
Visualization of congested nodes in experiment 1

## Slide 57
Experiment 2
6. Discussion and Preliminary Experiments
Case 1: and ; Case 2: and ; Case 3: and .
Solution of each iteration of ADMM in three cases and CPLEX

## Slide 58
Experiment 2
6. Discussion and Preliminary Experiments
Case 1: and ; Case 2: and ; Case 3: and .
Comparison of objective values of upper bound and CPLEX

## Slide 59
Experiment 2
6. Discussion and Preliminary Experiments
Visualization of congested nodes in experiment 2

## Slide 60
Dantzig-Wolfe decomposition algorithm
, ADMM and Projected Gradient method
Space-time-state network construction and network flow model
Required knowledge:
Dynamic Traffic Assignment and Vehicle Routing Problem
Time-dependent State-dependent shortest path problem
7. Summary

## Slide 61
References
Space-time-state network flow models and vehicle routing problem:
  1. Mahmoudi, M. and Zhou, X., 2016. Finding optimal solutions for vehicle routing problem with pickup and delivery services with time windows: A dynamic programming approach based on state–space–time network representations. Transportation Research Part B: Methodological, 89, 19-42.
  2. Liu, J., Kang, J., Zhou, X., Pendyala, R., 2018. Network-oriented household activity pattern problem for system optimization. Transportation Research Part C 94, 250-269
  3. Zhou, X., Tong, L., Mahmoudi, M., Zhuge, L., Yao, Y., Zhang, Y., Shang, P., Liu, J. and Shi, T., 2018. Open-source VRPLite Package for Vehicle Routing with Pickup and Delivery: A Path Finding Engine for Scheduled Transportation Systems. Urban Rail Transit, 4(2), 68-85.
Dynamic Traffic Assignment and Traffic flow model:
  4. Lu, C.C., Liu, J., Qu, Y., Peeta, S., Rouphail, N.M. and Zhou, X., 2016. Eco-system optimal time-dependent flow assignment in a congested network. Transportation Research Part B: Methodological, 94, pp.217-239.
  5. Zhou, X. and Taylor, J., 2014. DTALite: A queue-based mesoscopic traffic simulator for fast model evaluation and calibration. Cogent Engineering, 1(1), p.961345.
Dantzig-Wolfe Decomposition algorithm
  6. https://en.wikipedia.org/wiki/Dantzig%E2%80%93Wolfe_decomposition
Alternating Direction Method of Multipliers (ADMM)
  7. https://web.stanford.edu/~boyd/papers/pdf/admm_slides.pdf